## Slide 1: Unfolding Spectroheliogram MaGIXS*
P. S. Athiray, Amy Winebarger, MaGIXS team
University of Alabama in Huntsville
NASA MSFC
*The Marshall Grazing Incidence X-ray Spectrometer – First Working Slitless Solar X-ray Imaging Spectrometer
N VII
O VII
OVIII, VII
Fe XVII, VIII
Ne IX
MaGIXS (Solar coronal structures)
Chandra (O-type supergiant)
Nichols et al 2021
Savage et al 2023
Notes: Add an image of sun and chandra

## Slide 2: Objective
Characteristics of plasma heating in the solar corona
X-pixel
Y-pixel
Emission Measure Distribution (EMD)
Temperature, Density, Abundance, Emission Measure, Thermal/Ionization Equilibrium
Plasma Diagnostics – Holy Grail Data
Observable

## Slide 3
Culhane & Acton, 1974 “The Solar X-ray Spectrum”, ARAA, 12, 359
“... it is usually impossible to provide a single instrument with an acceptable combination of spatial, spectral, and time resolution to study flare events ...”
Is this still true? How to overcome?

## Slide 4
Diffraction (prism, grating…)
Slit imaging spectroscopy
Wavelength
Notes: Now if we remove the slit, here is what we get:

## Slide 5
Diffraction (prism, grating…)
Slitless imaging spectroscopy
Notes: The full extended source is now dispersed and it is now a bit harder to tell the origin of a photon that hit the detector, especially on the overlapping regions.

## Slide 6
Diffraction (prism, grating…)
SPECTRALLY PURE IMAGES
Notes: The role of the inversion is precisely to unfold that spectroheliogram by creating spectrally pure image from every emission line.

## Slide 7: Slit  Slitless imaging spectroscopy
p0 | p1 | p2 |  |  |  |  |  |  |  | 
Line intensity (Ph/pix) from a point on the Sun can be directly read off from detector pixels
Each detector pixel contains a linear combination of line intensities from several ions from different points on the Sun
Goal : Precisely determine the number of photons in every pixel from all observed emission lines
Detector Pixels
On–axis
Off–axis + 1
Off–axis - 1

## Slide 8: MaGIXS
MaGIXS data are ”overlappograms”
Observed several warm emission lines 1 to 5 MK plasma
30 July 2021, ~18:20 UT
~296 s science data
Multiple copies of same ions at different wavelengths offer constraints

## Slide 9: Unfolding method
Write a set of linear equations:
Observation = Response Matrix # EM
y = Mx
Response Matrix includes:
  Atomic data – How does the solar plasma radiate?
  Instrument response – How does the instrument measure the radiation?

## Slide 10
Sun EM: x0
M
Response matrix
2.8’’
Δθx2.8’’
pixel size:
Observation: y = Mx0
Notes: The sun that we observed has a certain emission measure. We can represent that emission measure with a 3D matrix ‘x’. To create that matrix, we slice the field of view into a large amount of pixels (there are more pixels than what I show here). And each of these boxes has a dem distribution. Basically that matrix tells you how much plasma you can find at a given position and a given temperature.
That plasma is going to emit X rays and these X rays will go into the instrument to create the observed data. As Athiray showed you, that process can simply be represented by a simple matrix multiplication equation: y=Mx

## Slide 11: Response Matrix
Atomic data – How does the solar plasma radiate?
Instrument response – How does the instrument measure the radiation?
Function of spectral pixels, spatial field angles, log T bins
Notes: Remove the plot ion the right..

## Slide 12
Response ‘M’
Flight data ‘y’
EM Cube
List of elementary spectra allowed by atomic physics convolved with instrument response
Solve for x# to match y using the ElasticNet Regularization method
x# = argmin[ ‖y-Mx‖22 + αρ‖x‖1 + 0.5α(1-ρ)‖x‖22 ]
Supervised Machine Learning – Inversion

## Slide 14: Questions

## Slide 16
Grating
Beam footprint subtends 34o
MaGIXS Instrument Design
Telescope section
Spectrometer section
Camera section
First mission to use deterministic polished X-ray mirrors
Athiray et al 2020,2021; Champey et al 2022 JAI
Slot
Notes: Initally it was a slit sp. Changed to slot , Bring a straw movie and aligning, them,

## Slide 17: Why inversion works?
MaGIXS field
335Å
Multiple copies of several ions observed at different wavelengths offer excellent temperature diagnostics
logt 6.0
logt 6.3
logt 6.4
logt 6.6
O VII
O VIII
Fe XVII
Ne IX
O VIII
Mg XI
Fe XVII
Fe XVII
Ne IX
N VII
C VI
O VII
O VIII
Fe XVII
Ne IX
O VIII
Fe XVII
Ne IX
N VII
C VI
O VII
O VIII
Fe XVII
Ne IX
O VIII
Mg XI
Fe XVII
Fe XVII
Ne IX
N VII
C VI
O VII
O VIII
N VII
C VI
Notes: Replace this with temperature slide

## Slide 18
DEM inversion – EM cube
Inversion works!